## Slide 1
Public risks of AV blocking
CJ Wu & Jonathan Wilson
117 DEM reports over 184 covered days in 2025
Risk matrix
30-day chance of ≥1 event at the impact tier
Likelihood | Insignificant 1 | Minor 2 | Significant 3 | Major 4 | Severe 5
Almost certain 5 | Medium | High | H7 Very high | Extreme | Extreme
Likely 4 | Medium | Medium | H3, H6 High | H1 Very high | Extreme
Moderate 3 | Low | Medium | H4, H5 Medium | High | H2* Very high
Unlikely 2 | Very low | Low | Medium | Medium | High
Rare 1 | Very low | Very low | Low | Medium | Medium
H1 Collision H2 Emergency obstruction* H7 Single AV blockage
H3 Transit H4 Ped/access H5 Occupant H6 Multi-AV
19.1
reports per 30 days
95% CI 15.8 to 22.9
24 min median duration
29.1% lasted ≥60 min
34 of 117 reports account for
74.3% of total logged event time
H2* uses inferred obstruction
at emergency scenes.
Explicit-only: Medium (2 × 4)
Logged event time does not measure medical delay or harm. Calendar-day rates lack trip or mileage exposure.
Source: SF DEM log, compiled/cleaned by Dr Missy Cummings. Jonathan Wilson pipeline, pinned 06fdb2e9.
Independent review: CJ Wu and team. Covered months: March and June–October 2025.
Notes: Public risks of AV blocking. Presenters: CJ Wu and Jonathan Wilson.
Source: San Francisco Department of Emergency Management incident log, compiled and cleaned by Dr Missy Cummings. Jonathan Wilson analysis pipeline, frozen commit 06fdb2e928ab133f799015ae01323c991669ddcd. The team independently reviewed calculations.
Primary source workbook: work/AV_Bricking/verification_20261004/source/av-blocking-analysis-06fdb2e928ab133f799015ae01323c991669ddcd/data/AV-Brick-Report.xlsx, sheet DEM Incidents. SHA256 cd01c0ec475a979b03dc74078dbd4ed97fc216d3342c9621f0ddf27051b60a54.
Independent frequency evidence: work/AV_Bricking/verification_20261004/frequency_current/frequency_verified.json. There are 120 full in-scope primary reports, but the frequency/recovery cohort is 117 reports in 184 covered days: March and June through October 2025. MLE rate = 117/184*30 = 19.0760869565 per 30 days, exact Poisson 95% CI [15.7764436531,22.8621895439]. Rounded slide values 19.1 and 15.8 to 22.9. This is a calendar-day report rate, without trip or mileage exposure.
Independent recovery evidence: work/AV_Bricking/verification_20261004/recovery_current/results.json. Median recorded duration is 24 minutes. 34/117 = 29.0598% of reports lasted at least 60 minutes. These reports account for 74.3330% of 6,222 total logged event minutes. Excluding the longest report, the share is 71.5786%. Durations are logged incident times, not actual medical delay, harm, passenger exposure, person-minutes, or total traffic delay.
Matrix source: work/AV_Bricking/verification_20261004/source/av-blocking-analysis-06fdb2e928ab133f799015ae01323c991669ddcd/project-site/assets/tables/tbl-risk-placement.csv and src/av_blocking/risk_matrix.py. This is the pinned rubric, not a direct estimate of injury probability. Likelihood uses the 30-day chance of at least one event at the governing impact tier. Cells: H1 AV-involved collision, Likely 4 × Major 4 = Very high. H2 emergency-response obstruction, Moderate 3 × Severe 5 = Very high, based on inferred obstruction at life-threatening emergency scenes. Using only explicitly stated obstructions gives Unlikely 2 × Major 4 = Medium. H3 transit/rail, Likely 4 × Significant 3 = High. H4 pedestrian/accessibility, Moderate 3 × Significant 3 = Medium. H5 occupant-related immobilization, Moderate 3 × Significant 3 = Medium. H6 multi-AV gridlock, Likely 4 × Significant 3 = High. H7 single-AV obstruction, Almost certain 5 × Significant 3 = Very high. H7 depends on the rubric's 60-minute Significant threshold.

## Slide 2
PUDO complaints per trip
BACKUP
2026 Q2 compared with the prior three quarters
Complaints per 100,000 trips
Chart: 
| 2025 Q3 | 2025 Q4 | 2026 Q1 | 2026 Q2
PUDO complaint rate | 1.5695 | 1.7607 | 1.7665 | 1.872
Prior 3 pooled rate: 1.71 per 100,000 trips
No clear evidence of
a rate difference
Latest quarter / prior 3 pooled
RR 1.09
95% CI 0.83 to 1.43
Exact two-sided p = 0.535
The interval includes a lower
and a higher rate.
This does not prove equality.
Complaints: 42, 66, 69, 79. Trips: 2.68M, 3.75M, 3.91M, 4.22M.
Source: instructor workbook ME 575 Class Final Data - PUDO - Waymo.xlsx, Sheet1!A7:D10.
Independent team calculation. PUDO means pickup/drop-off.
Notes: BACKUP slide. PUDO complaint rate comparison. This is a separate data source and metric from the DEM incident log.
Source: instructor workbook ME 575 Class Final Data - PUDO - Waymo.xlsx, Sheet1!A7:D10, SHA256 2459c381e620234fe62ce50f0b5ffcb55fc16e0aaefd03e0352e45fe44cbf729.
Quarter order: 2025 Q3, 2025 Q4, 2026 Q1, 2026 Q2. Complaints: 42,66,69,79. Trip exposure: 2,676,001;3,748,532;3,905,934;4,220,075. Rates = counts/trips*100,000: 1.5695061399453885, 1.760689251152184, 1.7665429062549445, 1.8720046444672191. Native editable bar chart stores rates rounded to six decimal places and displays two decimal places: 1.569506, 1.760689, 1.766543, 1.872005. Latest quarter is orange.
Prior 3 pooled exposure = 10,330,467 trips, complaints = 177, rate = 1.713378 complaints per 100,000 trips. Latest quarter rate = 1.872005. Latest/prior 3 rate ratio = 1.0925809. Exact conditional 95% CI = [0.8272003,1.4322201], exact two-sided p = 0.5353667. Rounded slide values: RR 1.09, CI 0.83 to 1.43, p 0.535. The interval and p-value do not show clear evidence of a rate difference. Failure to find a difference does not prove equal rates. Comparison assumes complaint counts and trip denominators are comparable across quarters.